CLI of ANT4000

(S/W Ver 303.3 or later)

Document version : 1.1

Date : 2014.4.17

- Document History

| Documemnt version | Changes | S/W version | Document Date |
| --- | --- | --- | --- |
| Ver 0.1 | Initial Release | 202.16 | 2011.2.14 |
| Ver 0.2 | Encoder : 4 commands added cli encapsulation [RTP/TS2UDP] cli coding [GOP/RandIntraCoded/ContIntraCoded] cli gop [0/60~65535] cli intra [60~65535] | 203.19E | 2011.5.25 |
| Ver 0.3 | Encoder : 4 commands added cli audiomode [Stereo/Mono/Off] cli audiodir [All/RX/RTSP] cli ledtest cli iframe Decoder : 1 command added cli ledtest *) ledtest command is only for particular OEM | 203.21 | 2011.6.23 |
| Ver 0.4 | Encoder : 2 commands added cli pcmcompress [None/aLaw/uLaw] cli pcm8kdown [Off/On] *) pcm8kdown is available only when H/W supports | 203.24 | 2011.7.5 |
| Ver 1.0 | Encoder : 1 command added cli mcttl [1~64] | 203.27 | 2011.9.20 |
| Ver 1.1 | Encoder & Decoder : old 5 commands documented cli serial cli serialbaud [1200/2400/….] cli serialstopbit [1/2] cli serialcsize [CS5/CS6/CS7/CS8] cli serialparity [DISABLE/ODD/EVEN] | 203.33 | 2014.4.17 |
| Ver 1.1 | Encoder : 1 command added cli encfres[Input/1920x1080P60/….] Decoder : 4 commands added cli rtsp [On/Off] cli rtspmode [P2P/Multicast] cli rtspgrp [ipaddr] cli rtspmcttl [1~64] | 303.00 | 2014.4.17 |

- Telnet port number, login ID and password

  - Port number: 8023

  - Login ID: root

  - Password: rootroot

Example)

>telnet 192.168.0.151 8023

>ID root

>password rootroot

- Commands for ENCODER

  - cli or cli help

cli eth [ipaddr] [mask]

cli gateway [ipaddr]

cli mode [P2P/Multicast]

cli intf [LAN/WIFI]

cli wifi

cli wifichannel [auto/36/44/52/60/149/157]

cli wifissid

cli grp [ipaddr]

cli peer [ipaddr]

cli mcttl [1~64]

cli peerstatus

cli localmachine

cli vinport [HDMI_1/HDMI_2/PC/AV]

cli sigstatus

cli video [On/Off]

cli encfres [Input/1920x1080P60/….]

cli encapsulation [RTP/TS2UDP]

cli coding [GOP/RandIntraCoded/ContIntraCoded]

cli gop [0/60~65535]

cli intra [60~65535]

cli cbr [0~50]

cli fps [0~85]

cli osd [On/Off]

cli rtsp [On/Off]

cli ainport [HDMI_1/HDMI_2/PC/AV]

cli audiomode [Stereo/Mono/Off]

cli pcmcompress [None/aLaw/uLaw]

cli pcm8kdown [Off/On]

cli audiodir [All/RX/RTSP]

cli serial

cli serialbaud [1200/2400/4800/9600/19200/38400/115200]

cli serialstopbit [1/2]

cli serialcsize [CS5/CS6/CS7/CS8]

cli serialparity [DISABLE/ODD/EVEN]

cli ledtest

cli iframe

cli allinfo

cli restart

cli save

  - cli allinfo

[ENC /root]# cli allinfo

== System Configuration ==

Local Machine Name : P2P Encoder

Local Machine S/W version : wimi4KV:303.03.3-r798-0

Eth IP : 192.168.0.249

Eth Mask : 255.255.255.0

Eth Mac : 00:04:3A:22:12:55

Gateway : 192.168.0.1

Streaming I/F : LAN

Streaming Mode : P2P

Wifi Channel : auto

Auto ChannelNo : unknown

Wifi SSID : NIMBUS_0012

Wifi Status : not working

Group IP(multicast) : 227.2.2.9

Peer IP(lan) : 192.168.0.234

Multicast TTL : 7

== Stream Configuration ==

Peer Machine Info : P2P Decoder, LAN(192.168.0.234)

Peer S/W version wimi4KV:303.03.3-r798-0

Peer Video Out Port : HDMI

Peer Output Resolution : D1920x1080P60

Video In Port : HDMI_1

Audio In Port : HDMI_1

Video Signal : detected

Input Resolution : D1920x1080P60

Encoding Resolution : 1920x1080P60

Color Space : RGB

HDMI Audio : PCM 48000

Streaming : Video-On / Audio-On / RTSP-On

Video Streaming : On

Encapsulation : RTP

Coding Mode : RandIntraCoded

GOP Size : 120

Intra Period : 120

Video Bitrate(Mbps) : 12

Frame Rate : 0

OSD Status : On

RTSP Server : On

Audio Streaming : Stereo

PCM Compress : None

PCM 8KHz DownSample : On

Audio Direction : RX

Baudrate : 9600

Stop Bit : 1

Character Size : CS8

Parity : DISABLE

Flow Control : None

  - cli eth

[ENC /root]# cli eth

Eth IP : 192.168.0.249

Eth Mask : 255.255.255.0

Eth Mac : 00:01:68:00:02:48

[ENC /root]# cli eth 192.168.0.247

Success Command

[ENC /root]# cli eth 192.168.0.249 255.255.0.0

Success Command

  - cli gateway

[ENC /root]# cli gateway

Gateway : 192.168.0.1

[ENC /root]# cli gateway 192.168.0.2

Success Command

  - cli mode

[ENC /root]# cli mode

Streaming Mode : P2P

[ENC /root]# cli mode Multicast

Success Command

[ENC /root]# cli mode P2P

Success Command

  - cli intf

[ENC /root]# cli intf

Streaming I/F : WIFI

[ENC /root]# cli intf LAN

Success Command

[ENC /root]# cli intf WIFI

Success Command

  - cli wifi

[ENC /root]# cli wifi

Wifi Channel : auto

Auto ChannelNo : unknown

Wifi SSID : NIMBUS_0012

Wifi Status : not working

  - cli wifichannel

[ENC /root]# cli wifichannel

Wifi Channel : 36

[ENC /root]# cli wifichannel auto

Success Command

[ENC /root]# cli wifichannel

Wifi Channel : auto

Auto ChannelNo : 64

  - cli wifissid

[ENC /root]# cli wifissid

Wifi SSID : NIMBUS_0012

  - cli grp

[ENC /root]# cli grp

Group IP(multicast) : 227.2.2.7

[ENC /root]# cli grp 227.2.2.5

Success Command

  - cli peer

[ENC /root]# cli peer

Peer IP(lan) : 192.168.0.234

[ENC /root]# cli peer 192.168.0.152

Success Command

  - cli mcttl

[ENC /root]# cli mcttl

Multicast TTL : 1

[ENC /root]# cli mcttl 5

Success Command

  - cli peerstatus

[ENC /root]# cli peerstatus

Peer Machine Info : None

[ENC /root]# cli peerstatus

Peer Machine Info : P2P Decoder, LAN(192.168.0.234)

Peer S/W version  wimi4KV:303.03.3-r798-0

Peer Video Out Port : HDMI

Peer Output Resolution : D1920x1080P60

  - cli localmachine

[ENC /root]# cli localmachine

Local Machine Name : P2P Encoder

Local Machine S/W version :  wimi4KV:303.03.3-r798-0

  - cli vinport

[ENC /root]# cli vinport

Video In Port : HDMI_1

[ENC /root]# cli vinport HDMI_2

Success Command

  - cli sigstatus

[ENC /root]# cli sigstatus

Video Signal : detected

Input Resolution : D1920x1080P60

Encoding Resolution : 1920x1080P60

Color Space : RGB

HDMI Audio : PCM 48000

Streaming : Video-On / Audio-On / RTSP-On

  - cli video

[ENC /root]# cli video

Video Streaming : On

[ENC /root]# cli video off

Success Command

  - cli encfres

[ENC /root]# cli encfres

Forced Enc Res : Input

[ENC /root]# cli encfres 1280x720P60

Success Command

[ENC /root]# cli encfres Input

Success Command

  - cli encapsulation

[ENC /root]# cli encapsulation

Encapsulation : RTP

[ENC /root]# cli encapsulation TS2UDP

Success Command

[ENC /root]# cli encapsulation RTP

Success Command

  - cli coding

[ENC /root]# cli coding

Coding Mode : RandIntraCoded

[ENC /root]# cli coding GOP

Success Command

[ENC /root]# cli coding RandIntraCoded

Success Command

[ENC /root]# cli coding ContIntraCoded

Success Command

  - cli gop

[ENC /root]# cli gop

GOP Size : 60

[ENC /root]# cli gop 120

Success Command

  - cli intra

[ENC /root]# cli intra

Intra Period : 120

[ENC /root]# cli intra 60

Success Command

  - cli cbr

[ENC /root]# cli cbr

Video Bitrate(Mbps) : 10

[ENC /root]# cli cbr 12

Success Command

  - cli fps

[ENC /root]# cli fps

Frame or Field Rate : 0

[ENC /root]# cli fps 30

Success Command

  - cli osd

[ENC /root]# cli osd

OSD Status : Off

[ENC /root]# cli osd on

Success Command

  - cli rtsp

[ENC /root]# cli rtsp

RTSP Server : On

[ENC /root]# cli rtsp off

Success Command

  - cli ainport

[ENC /root]# cli ainport

Audio In Port : HDMI_1

[ENC /root]# cli ainport PC

Success Command

  - cli audiomode

[ENC /root]# cli audiomode

Audio Streaming : Stereo

[ENC /root]# cli audiomode off

Success Command

[ENC /root]# cli audiomode mono

Success Command

[ENC /root]# cli audiomode stereo

Success Command

  - cli pcmcompress

[ENC /root]# cli pcmcompress

PCM Compress : aLaw

[ENC /root]# cli pcmcompress none

Success Command

[ENC /root]# cli pcmcompress alaw

Success Command

[ENC /root]# cli pcmcompress ulaw

Success Command

  - cli pcm8kdown

*) pcm8kdown is available only when H/W supports

[ENC /root]# cli pcm8kdown

PCM 8KHz DownSample : On

[ENC /root]# cli pcm8kdown off

Success Command

[ENC /root]# cli pcm8kdown on

Success Command

  - cli audiodir

[ENC /root]# cli audiodir

Audio Direction : All

[ENC /root]# cli audiodir rx

Success Command

[ENC /root]# cli audiodir rtsp

Success Command

[ENC /root]# cli audiodir all

Success Command

  - cli serial

[ENC /root]# cli serial

Baudrate : 9600

Stop Bit : 1

Character Size : CS8

Parity : DISABLE

Flow Control : None

  - cli serialbaud

[ENC /root]# cli serialbaud

Baudrate : 9600

[ENC /root]# cli serialbaud 38400

Success Command

  - cli serialstopbit

[ENC /root]# cli serialstopbit

Stop Bit : 1

[ENC /root]# cli serialstopbit 2

Success Command

ENC /root]# cli serialstopbit 1

Success Command

  - cli serialcsize

[ENC /root]# cli serialcsize

Character Size : CS8

[ENC /root]# cli serialcsize CS7

Success Command

[ENC /root]# cli serialcsize CS8

Success Command

  - cli serialparity

[ENC /root]# cli serialparity

Parity : DISABLE

[ENC /root]# cli serialparity ODD

Success Command

[ENC /root]# cli serialparity EVEN

Success Command

[ENC /root]# cli serialparity DISABLE

Success Command

  - cli ledtest

[ENC /root]# cli ledtest

Success Command

  - cli iframe

[ENC /root]# cli iframe

Success Command

  - cli save

[ENC /root]# cli save

Success Command

  - cli restart

[ENC /root]# cli restart

Success Command

- Commands for DECODER

  - cli help

[DEC /root]# cli help

cli eth [ipaddr] [mask]

cli gateway [ipaddr]

cli mode [P2P/Multicast]

cli intf [WIFI/LAN]

cli wifi

cli wifissid [string]

cli wifirxid [slave1~slave4]

cli grp [ipaddr]

cli peer [ipaddr]

cli peerstatus

cli localmachine

cli voutport [HDMI/COMPONENT/AV]

cli sigstatus

cli rtsp [On/Off]

cli rtspmode [P2P/Multicast]

cli rtspgrp [ipaddr]

cli rtspmcttl [1~64]

cli serial

cli serialbaud [1200/2400/4800/9600/19200/38400/115200]

cli serialstopbit [1/2]

cli serialcsize [CS5/CS6/CS7/CS8]

cli serialparity [DISABLE/ODD/EVEN]

cli ledtest

cli allinfo

cli restart

cli save

  - cli allinfo

[DEC /root]# cli allinfo

== System Configuration ==

Local Machine Name : P2P Decoder

Local Machine S/W version :  wimi4KV:303.03.3-r798-0

Eth IP : 192.168.0.234

Eth Mask : 255.255.255.0

Eth Mac : 00:0A:B4:33:01:13

Gateway : 192.168.0.1

Streaming I/F : LAN

Streaming Mode : P2P

Wifi RXID(multicast) : SLAVE1

Wifi SSID : NIMBUS_0BFE

Wifi Quality : not working

Group IP(multicast) : 227.2.2.7

Peer IP(lan) : 192.168.0.249

== Stream Configuration ==

Peer Machine Name : P2P Encoder , LAN(192.168.0.249

Peer S/W version :  wimi4KV:303.03.3-r798-0

Peer Video In Port : HDMI_1

Peer Audio In Port : HDMI_1

Peer Input Resolution : D1920x1080P60

Peer Encoding Resolution : 1920x1080P60

Peer HDMI Audio : PCM 48000

Video Out Port : HDMI

Display : D1920x1080P60

Streaming : Video-On / Audio-On / RTSP-On

RTSP Relay Server : On

Streaming Mode : P2P

Group IP(multicast) : 227.2.2.7

Multicast TTL : 1

Baudrate : 9600

Stop Bit : 1

Character Size : CS8

Parity : DISABLE

Flow Control : None

  - cli eth

Refer eth command of encoder

  - cli gateway

Refer gateway command of encoder

  - cli mode

Refer mode command of encoder

  - cli intf

Refer intf command of encoder

  - cli wifi

[DEC /root]# cli wifi

Wifi RXID(multicast) : SLAVE2

Wifi Channel : Unknown

Wifi SSID : WIMI4000_05B2

Wifi Quality : 5/5

  - cli wifissid

[DEC /root]# cli wifissid

Wifi SSID : WIMI4000_TEST

[DEC /root]# cli wifissid WIMI4000_05B2

Success Command

  - cli wifirxid

[DEC /root]# cli wifirxid

Wifi RXID(multicast) : SLAVE2

[DEC /root]# cli wifirxid slave1

Success Command

  - cli grp

Refer grp command of encoder

  - cli peer

Refer peer command of encoder

  - cli peerstatus

[DEC /root]# cli peerstatus

Peer Machine Name : P2P Encoder , LAN(192.168.0.249)

Peer S/W version :  wimi4KV:303.03.3-r798-0

Peer Video In Port : HDMI_1

Peer Audio In Port : HDMI_1

Peer Input Resolution : D1920x1080P60

Peer Encoding Resolution : 1920x1080P60

Peer HDMI Audio : PCM 48000

  - cli localmachine

[DEC /root]# cli localmachine

Local Machine Name : P2P Decoder

Local Machine S/W version : wimi4KV:303.03.3-r798-0

  - cli voutport

[DEC /root]# cli voutport

Video Out Port : HDMI

[DEC /root]# cli voutport COMPONENT

Success Command

  - cli sigstatus

[DEC /root]# cli sigstatus

Display : D1920x1080P60

Streaming : Video-On / Audio-On / RTSP-On

  - cli rtsp

[DEC /root]# cli rtsp

RTSP Relay Server : On

[DEC /root]# cli rtsp Off

Success Command

[DEC /root]# cli rtsp On

Success Command

  - cli rtspmode

[DEC /root]# cli rtspmode

Streaming Mode : P2P

[DEC /root]# cli rtspmode Multicast

Success Command

[DEC /root]# cli rtspmode P2P

Success Command

  - cli rtspgrp

[DEC /root]# cli rtspgrp

Group IP(multicast) : 227.2.2.7

[DEC /root]# cli rtspgrp 227.2.2.9

Success Command

  - cli rtspmcttl

[DEC /root]# cli rtspmcttl

Multicast TTL : 1

[DEC /root]# cli rtspmcttl 2

Success Command

  - cli serial

Refer serial command of encoder

  - cli serialbaud

Refer serialbaud command of encoder

  - cli serialstopbit

Refer serialstopbit command of encoder

  - cli serialcsize

Refer serialcsize command of encoder

  - cli serialparity

Refer serialparity command of encoder

  - cli ledtest

[ENC /root]# cli ledtest

Success Command

  - cli save

Refer save command of encoder

  - cli restart

Refer restart command of encoder